## Slide 1: Microprocessors, Microcontrollers, and Embedded Systems
CSE 315

## Slide 2: Information
Course teachers
  A. K. M. Mehedi Hasan Elin – MHE
  Md. Emamul Haque Pranta – EHP
Classes
  3 lectures per week
  First 2 weeks (MHE): Assembly language
  Middle 7 weeks (EHP): Microcontroller
  Last 5 weeks (MHE): Microprocessor

## Slide 3: CSE 316 Outline
Microprocessors, Microcontrollers, and Embedded Systems Sessional
  Assignments on assembly language
  Assignments on microcontrollers (ATmega32)
  Project on embedded systems

## Slide 4: Textbook for Assembly Language

## Slide 5: Textbook for Microprocessor

## Slide 6: A Typical Computer System Early days
Central Processor Unit
(CPU)
Input
Memory
Output

## Slide 7: A Typical Computer System Nowadays
CPU
Input
Memory
Output
Shared BUS

## Slide 8: Microprocessor
Microprocessor, by-itself, is completely useless
Many chips on mother board
BOOT ROM
Used at startup
Instruction (program) ROM
Keyboard Screen UART Parallel interface
etc
must have external peripherals to interact with outside
world
µP
CONTROL
ADDRESS
DATA
Transducers
Data RAM

## Slide 9
µP
CONTROL
ADDRESS
DATA
Microcontroller – put a limited amount of most commonly used resources “inside” the chip – a “limited” amount is often “enough” for many applications
BOOT ROM
Used at startup
Instruction (program) ROM
Transducers
UART Parallel interface
Etc
Data RAM
RAM
I/O PORTS
TIMER
ROM
MicroCONTROLLER
µC

## Slide 10: Uses of μC

## Slide 11: μP vs μC
 | μP | μC
Structure | CPU | CPU, memory, I/O
Uses | Computer system | Embedded system
Purpose | General | Specific
Cost | High | Low
No. instructions supported | Large | Fewer
Speed | Fast | Slower
Power consumption | High | Low
Architecture | von Neumann | Harvard

## Slide 12: Embedded systems
An embedded system is a computer system that has a dedicated function within a larger mechanical or electrical system
Usually based on microcontrollers
  Complex ones can have microprocessors too
Examples
  Automobiles and airplanes
  Medical devices
  Home appliances

## Slide 13: Embedded systems